## Slide 1: Integration Applications

## Slide 2: First Moments, Center of Gravity, Centroid

## Slide 3: Definitions
Center of Gravity: point in a body at which all the body’s mass could be concentrated without altering the effect that earth’s gravity has on the body.
Centroid: the equivalent to center of gravity for an area (since an area has no mass).
First Moments:
Moment of an area = area × distance to centroid
Moment of a volume = volume × distance to center of gravity
Moment of a mass = mass × distance to center of gravity

## Slide 4: First Moment of Area
Moment about x-axis, Mx:
Mx = (Area)(Distance from x-axis to Center)
Mx = (8 cm2 )(4 cm) = 32 cm3
Moment about y-axis, My:
My = (Area)(Distance from y-axis to Center)
My = (8 cm2 )(3 cm) = 24 cm3

## Slide 5: First Moment of Area
Circle:
Mx = (2.25π cm2 )(2 cm) = 14.1 cm3
My = (2.25π cm2 )(3 cm) = 21.2 cm3
Rectangle:
Mx = (2 cm2 )(-2 cm) = -4 cm3
My = (2 cm2 )(-4 cm) = -8 cm3
Mx = (Area)(Distance from x-axis to Center)
My = (Area)(Distance from y-axis to Center)

## Slide 6: Center of Gravity, Centroid
For simple shapes, the center of gravity or centroid is right smack in the middle (center of circle, center of sphere, center of rectangle, center of box, …).
For more complicated shapes, the body must be broken down into smaller, simpler areas or volumes in order to find the centroid or center of gravity. We can use the 1st Moment:

## Slide 7: Example 1: Find Centroid
4”
4”
4”
4”
2”
2”
Set up a coordinate system and find the center of each section. Then find the 1st Moment for each Section
(0,0)
l (5,1)
l
(6,4)
l (5,8)
1st Moment about y-axis:
Bottom Block:
Middle Block:
Top Block:

## Slide 8: Example 1
Another Way to View This: The center of each section simply gets weighted by that section’s percentage of the total area.
4”
2”
(0,0)
4”
4”
4”
2”
l (5,1)
l
(6,4)
l (5,8)
1st Moment about x-axis:
Bottom Block:
Middle Block:
Top Block:

## Slide 9: Example 1
Does the answer seem reasonable?
4”
4”
4”
4”
2”
2”
(0,0)
l (5,1)
l
(6,4)
l (5,8)

## Slide 10: Center of Gravity, Centroid
Coordinates of Center of Rectangle:
Area of Rectangle:
(y2 – y1)dx

## Slide 11: Example 2
Find the centroid of the deck of the ship with respect to the origin indicated.
(0,0)
)

## Slide 12: Example 2
Find the centroid of the deck of the ship with respect to the origin indicated.
(0,0)
From Homework #7:
A = 433.6735 ft2

## Slide 13: Example 2
A = 433.6735 ft2
>> A = 433.6735;
>> f = sym('x*(-3/392*(x-28)^2+6-(3/392*(x-28)^2-6))');
>> xbar = 1/A*int(f,'x',0,50)
xbar =384236496379668921875/14123288431433875456
>> xbar = double(xbar)
xbar = 27.2059

## Slide 14: Example 2
(0,0)

## Slide 15: Example 3
The airplane rudder pictured below consists of one quadrant of an ellipse and one quadrant of a circle. Find the coordinates of the centroid.
Equation of Circle:
Equation of Ellipse:
Origin

## Slide 16: Example 3
This is no fun to do by hand!
Area of quarter circle:

## Slide 17: Example 3
>> A = 1/4*(pi*1.2^2 + pi *1.2*2);
>> f = sym('x*(sqrt(4 - 4*x^2/1.44)+sqrt(1.44-x^2))');
>> x_bar = 1/A*int(f, 'x',0,1.2)
x_bar = 0.50929581789406509528816968668252

## Slide 18: Example 3
>> f = sym('(4 - 4*x^2/1.44)-(1.44-x^2)');
>> y_bar = 1/(2*A)*int(f,'x',0,1.2)
y_bar = 0.33953054526271006352544645778835

## Slide 19: Example 3
Does the answer seem reasonable?
Origin